## Slide 1
Validating Cell Tower Clustering For Mobility Prediction
Pedro d'Aquino
Mehrdad Moradi
Dec. 13, 2012

## Slide 2: Cellular Mobility Prediction is in Operators’ Interest
Network Optimizations:
  Resource Pre-allocation
  Prefetching
  Handover Optimization
Personalized Services
  Location Based Offline Advertisement

## Slide 3: Current Approaches
Instrumentation of User devices for Collecting:
  GPS/WiFi/GSM
  Application
Using General Performance Event Handling(GPEH) Data:
  Radio Measurement
  Cell Information
  Calls

## Slide 4: GSM Data Sets
 | Cells | Area Codes | Country IDs | Cell Transitions | Status
Nokia Challenge | 23378 | 966 | 32 | 3308612 | Sampled
Reality Mobility | 32787 | 1052 | 2 | 619693 | Transition based

## Slide 5: Our Approach
Mobility Path Extraction
Oscillating Pair Detection
Oscillation Graph Generation
Oscillation Graph Clustering
Clustering Efficiency Evaluation

## Slide 6: Mobility Path Extraction
Input: GSM Logs
Output: Mobility Paths
Person Id | T start | T end |  | Cell Id
1 | 0 | 4 | 4 | C1
1 | 6 | 9 | 3 | C4
1 | 9 | 13 | 4 | C3
1 | 15 | 24 | 9 | C7
1 | 24 | 28 | 4 | C5
[ C1 C4 C3 C7]
[C7 C5]
:T end – T Start <
=5

## Slide 7: Oscillating Pair Detection
Goal:
  Retrieve sets of towers that overlap each other in all mobility paths:
    Soft Handover: The user is in a stationary state but there is transition between overlapping towers.
Solution:
  Switching: a handover from one tower to another inside of a mobility path
  Ex[ x, y, x, w, v, w, y], minimum switching count= 3
    (x,y) has 3 switches
      It is an oscillating pair

## Slide 8: Oscillation Graph Generation
G(V, E):
  V: All cell towers in oscillating pairs
  E: Weighted edges with weight:
  connecting oscillating pairs.
Intuition:
  s(x,y) is the ratio of how many times the cell towers x and y oscillated over the number of mobility paths in which x and y appear.
  Example: [ x, y, x, w, v, w, y], [x f y], [x y g]: s(x,y)=1/3

## Slide 9: Oscillation Graph Clustering
Approach:
  Greedy Algorithm:
    Removing edge with minimum weight
    Finding cluster C:
      Quality Metric(Q(C) ) >threshold

## Slide 10: Oscillation Graph Clustering(2)
Intuition:
0.6
0.9
0.8
0.1
0.8
0.75
0.9
0.6
0.9
0.8
0.8
0.75
0.9
Removing lowest weight edge
0.9
0.9
0.9
0.9
0.9
0.6
0.9
0.8
0.8
0.75
0.9
0.9
Cluster 1
Cluster 2
Quality Threshold= 1.5, max size cluster = 4
Quality(C1)=3.2 >1.5
Quality(C2)=3.15 >1.5
Quality(C2)=3.15 >1.5, Cluster Size=8> 4

## Slide 11: Questions
How much clustering is accurate?
Are clustered cells are near enough to overlap?
Does sampling cause high rate of loss in mobility paths?

## Slide 12: Clustering Efficiency Evaluation
Sampling Effect:
  Comparing the effect of sampling on Reality Mining dataset
Metric Measurements:
  Comparing the results of the clustering in datasets.
    Cluster Distance
    Cluster Incompleteness
Cross Validation:
  Validating cluster characteristic using GPS data sets:
    OpenCelld
    OpenBMap

## Slide 13: Clustering: Sampling Effect (1)
Reality Mining dataset logs every cell transition
  We have many soft handovers in one minutes.
    Question: Do we really need such precision?
Nokia Mobile Data Challenge the active cell tower connection is sampled every minute.
  We lose many hard handovers in one minutes.
  Question: Are we really ignoring many mobilities?

## Slide 14: Clustering: Sampling Effect
Sampling every one minute doesn’t change distribution of size and quality.

## Slide 15: Clustering: Density Ratio
Sampling every one minutes doesn’t change density ratio:
  Density Ratio= (# Clusters/ # Cells) in an area

## Slide 16: GPS Data Sets(1)
Nokia Mobile Data Challenge – GPS
  GSM and GPS entries do not necessarily have the same timestamp
    Intuition: Average of all GPS positions that were associated with that tower
    How much accurate the GPS estimate of a particular tower is?
      Standard deviation
        Haversine formula

## Slide 17: GPS Data Sets (2)
  Cost:
    k: is the number of users in the dataset
    m,n: upper bounds on the number of GPS
    and GSM records per user
OpenCellId and OpenBMap:
  keeps track of the position and associates it with a cell tower

## Slide 18: GPS Data Sets (3)
  Combine OpenBMap and OpenCellId measures and use an average
Summary:

## Slide 19: MDC GPS VS OpenCellID
Distance is usually small…
  confidence in the MDC GPS logs

## Slide 20: Metric Measurements: Cluster Distance
Cluster Distance:
  The average distance between cells in a cluster
  Closeness: group together towers that are geographically close

## Slide 21: Metric Measurements: Incompleteness
Incompleteness:
  The number of cells within meters of specific cell, but not clustered with that cell
  Dual of the cluster distance

## Slide 22: Conclusion

## Slide 23: Future Works