## Slide 1
Validating Cell Tower Clustering For Mobility Prediction
Pedro d'Aquino
Mehrdad Moradi
Dec. 13, 2012

## Slide 2: Cellular Mobility Prediction is Operators’ Interest
Network Optimizations:
  Resource Pre-allocation
  Prefetching
  Handover Optimization
Personalized Services
  Location Based Offline Advertisement

## Slide 3: Current Approaches
Instrumentation of User devices for Collecting:
  GPS/WiFi/GSM
  Application
Using General Performance Event Handling(GPEH) Data:
  Radio Measurement
  Cell Information
  Calls

## Slide 4: Data Sets
 | Cells | Area Codes | Country IDs | Cell Transitions | Status
Nokia Challenge | 23378 | 966 | 32 | 3308612 | Sampled
Reality Mobility | 32787 | 1052 | 2 | 619693 | Transition based

## Slide 5: Our Approach
Mobility Path Extraction
Oscillating Pair Detection
Oscillation Graph Generation
Oscillation Graph Clustering
Clustering Efficiency Evaluation

## Slide 6: Mobility Path Extraction
Input: GSM Logs
Output: Mobility Paths
Person Id | T start | T end | T duration | Cell Id
1 | 0 | 4 | 4 | C1
1 | 6 | 9 | 3 | C4
1 | 9 | 13 | 4 | C3
1 | 15 | 24 | 9 | C7
1 | 24 | 28 | 4 | C5
[ C1 C4 C3 C7]
[C7 C5]

## Slide 7: Oscillating Pair Detection
Goal:
  Retrieve sets of towers that overlap each other in all mobility paths:
    Soft Handover: The user is in a stationary state but there is transition between overlaping towers.
Solution:
  Switching: a handover from one tower to another inside of a mobility path
  Ex[ x, y, x, w, v, w, y], minimum switching count= 3
    (x,y) has 3 switches
      It is oscillating pair

## Slide 8: Oscillation Graph Generation
G(V, E):
  V: All cell towers in oscillating pairs
  E: Weighted edges with weight:
  connecting oscillating pairs.
Intuition:
  s(x,y) is the ratio of how many times the cell towers x and y oscillated over the number of mobility paths in which x and y appear.
  Example: [ x, y, x, w, v, w, y], [x f y], [x y g]: s(x,y)=2/3

## Slide 9: Oscillation Graph Clustering
Approach:
  Greedy Algorithm:
    Removing edge with minimum weight
    Finding cluster C:
      Quality Metric(Q(C) ) >threshold

## Slide 10: Oscillation Graph Clustering(2)
0.6
0.9
0.8
0.1
0.8
0.75
0.9
0.6
0.9
0.8
0.8
0.75
0.9
Removing lowest weight edge
0.9
0.9
0.9
0.9
0.9
0.6
0.9
0.8
0.8
0.75
0.9
0.9

## Slide 11: Questions
How much clustering is accurate?
Are clustered cells are near enough to overlap?
Does sampling cause high rate of loss in mobility paths?

## Slide 12: Clustering Efficiency Evaluation
Comparing the effect of sampling on Reality Mining dataset
Comparing the results of the clustering in datasets.
  Cluster Distance
  Cluster Incompleteness
Validating cluster characteristic using GPS data sets:
  OpenCelld
  OpenBMap

## Slide 13: Clustering: Sampling Effect
Sampling every one minute doesn’t change distribution of size and quality.

## Slide 14: Clustering: Ratio
Sampling every one minutes doesn’t change density ratio:
  Density Ratio= (# Clusters/ # Cells) in an area

## Slide 15: Clustering: Density Ratio
Sampling every one minutes doesn’t change density ratio:
  Density Ratio= (# Clusters/ # Cells) in an area

## Slide 16: GPS Data From MDC

## Slide 17: MDC GPS VS OpenCellID

## Slide 18: Cluster Distance

## Slide 19: Cluster Incompleteness

## Slide 20: Conclusion

## Slide 21: Future Works